## Slide 1: ENGINEERING STATISTICS
PRESENTED BY
Dr. R. VIJAYAKUMAR
Assistant Professor
Department of Statistics
St. Joseph’s College (Autonomous)
Tiruchirappalli – 620 002

## Slide 2: Introduction
Statistical Quality Control is one of the most important
applications of the statistical techniques in industry.
Control
The actual performance and compare it with some
standard.
Quality Control
Quality control can be defined as the entire collection of
activities which ensures that the operation will produce
the optimum quality products at minimum cost.

## Slide 3
Quality control, covers all the factors
Quality of Materials
Quality of Manpower
Quality of Machines
Quality of Management

## Slide 4: Benefits of S.Q.C
S.Q.C. is the control, maintenance and improvement in the quality standards.
S.Q.C. involves the identification and elimination of assignable causes of variation and possibly the inclusion of good ones.
A process in control is predictable.
It provides better quality assurance at lower inspection cost.
S.Q.C reduce waste of time and material to the absolute minimum by giving an early warning about the occurrence of defects.

## Slide 5: Causes of Variation
Variation in the quality of manufactured product in the
repetitive process in industry is inherent and inevitable
Types of causes
There are two types of causes namely
1. Chance causes.
2. Assignable causes.

## Slide 6
Chance causes
Some “stable pattern of variation “or “a constant cause
system” is inherent in any particular scheme of Production and
inspection. This pattern results from many minor causes that
behave in a random manner.
Assignable causes
This type of variation attributed to any production process is
due to non – random or the so-called assignable causes and is
termed as preventable variation.

## Slide 7: DISTINGUISH BETWEEN CHANCE AND ASSIGNABLE CAUSES
Chance causes of Variation | Assignable causes of Variation
Consist of many individual causes. | Cost of just a few individual causes.
Any one chance cause results in only a small amount of variation. | Any one assignable causes can result in a large amount of variation.
Chance variation cannot economically be eliminated from a process | The presence of assignable variation can be detected and action to eliminate the causes is usually economically justified.
Some typical chance causes of variation are: Slight vibration of a machine. Lack of human perfection in reading instruments and setting controls. Voltage fluctuations and variation in temperatures. | Some typical assignable causes of variation are: Negligence of operators. Defective raw material. Faulty equipment. Improper handling or machines.

## Slide 8: The main objective in any production process is to control and maintain a satisfactory quality level of the manufactured product so that it conforms to specified quality standards.
Process Control
Product Control
Product control mean controlling the quality of the product by critical examination at strategic points and this is achieved through ‘Sampling Inspection Plans’ pioneered by H.F. Dodge and H.C. Romig. Product control aims at guaranteeing a certain quality level to the consumer regardless of what quality level is being maintained by the producer.

## Slide 9
PROCESS CAPABILITY
Process capability may be defined as the “minimum spread of a specific measurement variation which will include 99.7% of the measurements from the given process”. In other words, process capability = 6σ since 6σ is taken as a measure of the spread of the process, which is also called natural tolerance.

## Slide 10
Techniques of S.Q.C
Process Control
Product Control
Variables
Attributes
Variables
Attributes
X bar Chart
R-Chart
σ -Chart
C-Chart
np-Chart
p-Chart

## Slide 11
CONTROL CHARTS
A control chart is a graphical representation of the collected information. The information any pertain to measured quality characteristics or judged quality characteristics of samples.
CONTROL LIMITS
These are limits of sampling variation of a statistical measure such that if the production process is under control, the values of the measure calculated from different rational sub-groups will lie within these limits. Points falling outside control limits indicate that the process is not operating under a system of chance causes.

## Slide 12
SPECIFICATION LIMITS
An article is proposed to be manufactured, the manufactures have to decide upon the maximum and the minimum allowable dimensions of some quality characteristics so that the product can be gainfully utilized for which it is intended. If the dimensions are beyond these limits, the product is treated as defective and cannot be used.
Tolerance limits
These are limits of variation of a quality measure of the product between which at least a specified proportion of the product is expected to lie, provided the process is in a state of statistical quality control.